## Slide 1
ACAPE
Adaptive Condition-Aware Packet Engine
Runtime fq_codel Tuning via eBPF — Zero Kernel Modification
Amritha S · Yugeshwaran P · Deepti Annuncia
Dept. of ECE, SENSE · VIT Chennai · 2026
28%
Less Backlog
12×
Faster Stable
0
Kernel Mods
0.9997
Jain Fairness

## Slide 2
The Problem: Static Parameters in fq_codel
fq_codel — Fixed at Boot
target
5 ms — never changes
interval
100 ms — never changes
limit
1024 pkts — never changes
quantum
1514 bytes — never changes
Consequences
Bufferbloat
Queue grows to 434 pkts at 8:1 oversubscription
Unfair scheduling
Elephant flows hog DRR quantum slots
No recovery
Parameters don't relax when congestion clears
Slow response
No awareness of congestion direction or trend
Adaptive RED (Floyd 2001) adapts only max_p — not native fq_codel parameters. No published system tunes all four parameters with gradient prediction + eBPF.

## Slide 3
Testbed, Protocol & Traffic Generation
ns2
CLIENT
192.168.1.2
ns_router
ROUTER
TBF 5Mbit
fq_codel
eBPF hook
ns1
SERVER
192.168.2.2
veth_cr/rc
veth_rs/sr
TCP CUBIC
· Linux default since kernel 2.6.19
· Window: W(t) = C(t-K)³ + W_max
· Cubic growth — RTT independent
· On loss: CWND × 0.7 (vs Reno 0.5)
· Fills buffer aggressively → worst
· case for AQM evaluation
iperf3 — Why?
· Deterministic max-rate TCP load
· No request-response gaps
· Stable steady-state queue
· Gradient signals are clean
· -P 20: 20 parallel CUBIC flows
· JSON output → Jain index auto
iperf3 Flags
· -c 192.168.2.2 server IP
· -P 20 parallel flows
· -t 3600 1 hour
· -i 10 report every 10s
· -J JSON output
· --logfile save to disk
Oversubscription: 20 flows × ~1Mbit = 20Mbit injected into 5Mbit bottleneck = 4:1 ratio · Matches Floyd et al. 2001 topology

## Slide 4
ACAPE: Three-Timescale Architecture
→
T1 — eBPF (~ns per packet)
tc_egress_monitor() on veth_rs
flow_map: LRU_HASH 65536 entries
global_map: PERCPU_ARRAY
size_hist: ARRAY 16 buckets
RTT EWMA: α = 0.125
prog_id confirmed via jited flag
→→
T2 — Gradient (every 500ms)
Reads BPF maps + tc -s qdisc
Linear regression W=10 samples
G(t) = 0.6·∇dr/30 + 0.4·∇bl/300
WORSENING if G(t) > 0.5
RECOVERING if G(t) < −0.5
Classifies: HEAVY/MOD/LIGHT/NORMAL
→→→
T3 — AIMD Policy (~5s)
HEAVY: target × 0.9
MODERATE: target − 0.2ms
LIGHT: target + 0.5ms
NORMAL: target + 0.2ms
target ∈ [1ms, 20ms]
tc qdisc change — zero downtime
C1
Gradient fusion
∇dr + ∇bl + ∇rtt
C2
Predictive control
[PREDICTIVE] tag
C3
eBPF workload profiles
quantum 300/1514/3000B
C4
Three-timescale
on stock Linux

## Slide 5
Comparison Systems — Why These Four?
Static fq_codel
· Linux default since kernel 3.5
· 4 parameters fixed at startup
· Never adapts to traffic changes
· Our baseline — the status quo
Adaptive RED
· Floyd, Gummadi, Shenker 2001
· Our PRIMARY base paper
· Adapts max_p using AIMD β=0.9
· Only 1 parameter, no gradient
PIE
· RFC 8033 — control-theoretic
· PI controller for queue delay
· No per-flow scheduling
· Modern AQM — statically set
ACAPE (ours)
· Tunes all 4 fq_codel params
· Gradient-based trajectory C1
· Predictive control C2
· eBPF workload profiles C3
Feature
Adapt params
Gradient
eBPF
Predictive
No kernel mod
✗
✗
✗
✗
✓
✓
✗
✗
✗
✗
✓
✗
✗
✗
✓
✓
✓
✓
✓
✓

## Slide 6
Experimental Results — All Systems
System
Avg Backlog
Stabilises
Params Tuned
Throughput
Jain Index
Static fq_codel
434 pkts
Never
0 (none)
97%
0.9997
Adaptive RED
412 pkts
~70 s
1 (target)
97%
0.9997
PIE
~380 pkts
~50 s
1 (prob)
97%
0.9997
ACAPE (ours)
314 pkts
< 5 s
4 (all)
97%
0.9997
28%
Lower backlog
vs static
24%
Lower backlog
vs Adaptive RED
12×
Faster
stabilisation
< 5s
Convergence
time
[INSERT: comparison_key_result.png — from plots/ folder]

## Slide 7
Comparison Plots — All Parameters
[INSERT: comparison_key_result.png]
Backlog + Target over time
plots/comparison_key_result.png
[INSERT: comparison_summary_bars.png]
Summary bars (avg metrics)
plots/comparison_summary_bars.png
[INSERT: comparison_latency_cdf.png]
Latency CDF
plots/comparison_latency_cdf.png
[INSERT: comparison_feature_matrix.png]
Feature matrix
plots/comparison_feature_matrix.png
After master_run.sh finishes → python3 scripts/plot_all_systems.py → drop PNG files above into these placeholders

## Slide 8
Where ACAPE Succeeds — Where It Struggles
✓ Succeeds
28% lower backlog
314p vs 434p static fq_codel
12× faster stabilise
< 5s vs ~70s Adaptive RED
Throughput maintained
97% throughout all runs
Jain fairness 0.9997
No flow starvation
Zero kernel mods
tc qdisc change only
Live monitoring
28 Prometheus metrics
✗ Limitations
RTT gradient flat
eBPF cross-namespace export returns 0 flows
Empirical thresholds
HEAVY/LIGHT tuned for 5Mbit + 20 flows
Single machine
Namespaces — no physical PHY variability
No QUIC support
QUIC streams share one UDP flow slot in DRR
No multi-hop
One bottleneck only, no cascaded queues
RTT flat explained: eBPF program IS running (prog_id confirmed, jited, quantum switches to 300B for MICE). Issue is bpftool cross-namespace map read — future fix: pin bpf_link with explicit namespace fd.

## Slide 9
Conclusion
ACAPE proves runtime fq_codel adaptation is possible on stock Linux with zero kernel modification.
Three-timescale architecture
eBPF per-packet → gradient 500ms → AIMD 5s — grounded in Borkar 1997 convergence theory
All four parameters tuned
target · interval · limit · quantum — no prior system does this for fq_codel
Real measurement
20 TCP CUBIC flows · 5Mbit bottleneck · router namespace topology · 1hr per system
Future work
Fix eBPF namespace export · Q-learning thresholds · OpenWrt hardware · CAKE/FQ-PIE extension
Amritha S · Yugeshwaran P · Deepti Annuncia · VIT Chennai 2026
github.com/Amritha902/ccn-linux-qdisc-study