## Slide 1
TCP Protocol Used: TCP CUBIC
Why TCP CUBIC?
Linux kernel default since 2.6.19
Verify: sysctl net.ipv4.
tcp_congestion_control
→ returns: cubic
Most common TCP variant
deployed globally
Fills buffers aggressively
→ worst case for AQM
Any AQM that handles CUBIC
handles all TCP variants
CUBIC Window Function
W(t) = C(t − K)³ + W_max
C
= 0.4 (scaling constant)
t
= time since last loss event
K
= time to reach W_max without loss
W_max
= window at last congestion event
On Packet Loss
CWND ← CWND × 0.7
(TCP Reno uses 0.5)
vs Other Variants
Reno: 0.5x / BBR: rate-based / CUBIC: 0.7x cubic
CUBIC Behavior in Our Testbed
20 flows × CUBIC
Each flow independently
probes for bandwidth
4:1 oversubscription
20×~1Mbit into 5Mbit
creates sustained queue
Fills buffer fast
Reaches 400+ pkts quickly
before backing off
Bursty window growth
Cubic shape means
aggressive probing
RTT insensitive
Unlike Reno, CUBIC
ignores RTT in growth
TCP CUBIC RFC 8312 · Ha, Rhee, Xu — ACM SIGOPS 2008 · Linux kernel source: net/ipv4/tcp_cubic.c

## Slide 2
Traffic Generator: iperf3 — Full Specification
What is iperf3?
iperf3 v3.16 — Network bandwidth measurement tool by ESnet (Lawrence Berkeley National Lab). Generates deterministic TCP/UDP flows between server and client processes.
Why iperf3, not real application traffic?
Real apps (HTTP/2, DASH video) have request-response gaps that create variable queue states — gradient signals become noisy. iperf3's constant-rate injection produces a deterministic steady-state queue.
Mode: TCP
NOT UDP mode
TCP = congestion control
responds to drops
UDP = fixed rate
ignores drops
not realistic
TCP tests the AQM's
ability to signal
congestion correctly
Exact Command Used — Every Flag Explained
-c 192.168.2.2
Connect to server at this IP (ns1 server namespace)
-p 5202
Port 5202 — avoids conflict with system services on 5201
-P 20
20 parallel TCP CUBIC connections simultaneously
-t 3600
Run for 3600 seconds = 1 hour per system
-i 10
Report per-flow throughput every 10 seconds
-J
Output in JSON format (machine-readable, parsed for Jain index)
--logfile X.json
Save JSON output to disk — preserved after process ends
SERVER (ns1): iperf3 -s -p 5202 CLIENT (ns2): iperf3 -c 192.168.2.2 -p 5202 -P 20 -t 3600 -i 10 -J --logfile logs/X.json

## Slide 3
Implementation: Router Topology Setup Commands
Namespace + veth Creation
# Create 3 isolated namespaces
ip netns add ns2 # client
ip netns add ns_router # router
ip netns add ns1 # server
# Client <-> Router veth pair
ip link add veth_cr type veth \
peer name veth_rc
ip link set veth_cr netns ns2
ip link set veth_rc netns ns_router
# Router <-> Server veth pair
ip link add veth_rs type veth \
peer name veth_sr
ip link set veth_rs netns ns_router
ip link set veth_sr netns ns1
IP + Route + TBF + fq_codel
# Assign IPs
ip netns exec ns2 ip addr add \
192.168.1.2/24 dev veth_cr
ip netns exec ns_router ip addr add \
192.168.1.1/24 dev veth_rc
ip netns exec ns_router ip addr add \
192.168.2.1/24 dev veth_rs
ip netns exec ns1 ip addr add \
192.168.2.2/24 dev veth_sr
# IP forwarding in router
ip netns exec ns_router \
sysctl -w net.ipv4.ip_forward=1
# TBF 5Mbit bottleneck on router
ip netns exec ns_router tc qdisc \
add dev veth_rs root handle 1: \
tbf rate 5mbit burst 16kbit \
latency 400ms
Verify: ip netns exec ns2 ping -c 3 192.168.2.2 → 0% packet loss confirms router forwarding works

## Slide 4
Implementation: eBPF Attach + fq_codel + Controller
eBPF Compile + Attach
# Compile eBPF program
# -O2: optimise for speed
# -g: embed BTF type info
# -target bpf: eBPF ISA
clang -O2 -g -target bpf \
-c ebpf/tc_monitor.c \
-o ebpf/tc_monitor.o
# Attach clsact qdisc
ip netns exec ns_router \
tc qdisc add dev veth_rs clsact
# Attach eBPF to egress
ip netns exec ns_router \
tc filter add dev veth_rs \
egress bpf direct-action \
obj tc_monitor.o \
sec tc_egress
# Verify: jited = JIT ok
tc filter show dev veth_rs \
egress
# → id 49152 jited
Apply fq_codel (each system)
# Remove old child qdisc
tc qdisc del dev veth_rs \
parent 1:1 2>/dev/null
# static_fqcodel
tc qdisc add dev veth_rs \
parent 1:1 handle 10: \
fq_codel target 5ms \
interval 100ms \
limit 1024 quantum 1514
# PIE
tc qdisc add dev veth_rs \
parent 1:1 handle 10: pie \
target 15ms limit 1000 \
tupdate 30ms
# ACAPE: same base as static
# controller adjusts at runtime
# via: tc qdisc change ...
# Verify live
tc -s qdisc show dev veth_rs
ACAPE Controller (key part)
# T3 — tc qdisc change
# Applied every ~5 seconds
# No traffic interruption
tc qdisc change \
dev veth_rs \
parent 1:1 handle 10: \
fq_codel \
target {X}us \
interval {Y}us \
limit {Z} \
quantum {Q}
# X = target_ms × 1000
# Y = interval_ms × 1000
# Z = limit packets
# Q = 300/1514/3000
# Log format:
[PREDICTIVE] HEAVY->MOD
target=4.50ms limit=921
quantum=300 adj=3
# 15 adjustments in 10min
# 5.00->4.50->4.05->...->1.03
BPF maps: flow_map (LRU_HASH 65536) tracks per-flow state · global_map (PERCPU_ARRAY) aggregate counters · size_hist (ARRAY 16 buckets) packet sizes

## Slide 5
Metrics: What We Measure, How, and Why
Queue Backlog (pkts)
HOW: tc -s qdisc show | grep backlog
WHY: Primary bufferbloat indicator. Static=434p. ACAPE=314p. 28% lower.
Throughput (Mbps)
HOW: iperf3 JSON: sender.bits_per_second
WHY: Must stay ≥97% of 5Mbit. Confirms AQM doesn't collapse the link.
Drop Rate (/s)
HOW: tc dropped counter delta / time
WHY: High drops + low backlog = correct CoDel behaviour. AQM signalling TCP early.
fq_codel target (ms)
HOW: tc -s qdisc | grep target (in microseconds)
WHY: Our actuation signal. Static stays 5ms. ACAPE drives 5→1ms staircase.
Sojourn Time (ms)
HOW: Little's Law: backlog / (throughput / pkt_size)
WHY: Queue wait per packet. High sojourn = bufferbloat. ACAPE reduces this.
Jain Fairness Index
HOW: J=(Σxi)²/(n·Σxi²) from iperf3 per-flow rates
WHY: 1.0 = perfect fairness. We maintain 0.9997 throughout despite aggressive tuning.
Composite Gradient G(t)
HOW: 0.6·∇dr/30 + 0.4·∇bl/300 (linear regression W=10)
WHY: Novel C1. Detects direction of congestion change. >0.5=WORSENING.
Regime Code (0-3)
HOW: Threshold classify on drop_rate + backlog
WHY: 0=NORMAL 1=LIGHT 2=MODERATE 3=HEAVY. Drives AIMD update rule selection.
All metrics collected every 1s to CSV · 28 metrics exported to Prometheus port 9101 · Grafana dashboard: localhost:3000/d/acape2026