## Slide 1
Feature-by-Feature
Comparison
Static fq_codel · Adaptive RED · PIE · CAKE · ACAPE
One slide per feature — 12 features total
Static fq_codel
Adaptive RED
PIE
CAKE
ACAPE (ours)
VIT Chennai 2026 · Amritha S · Yugeshwaran P · Deepti Annuncia
▶ Introduce: We will now go through each feature one by one, showing which system has it and what it actually does.

## Slide 2
Feature 1 of 12
Feature 1 of 12
Tunes fq_codel target parameter
The target parameter defines the maximum sojourn time (packet wait) before CoDel begins dropping. Lower target = more aggressive dropping = smaller queue. Static systems fix this at 5ms forever. Adaptive systems vary it based on congestion.
Static fq_codel
✗ MISSING
Fixed at 5ms
at startup.
Never changes
regardless of
traffic.
Result:
Queue builds to
400+ packets.
Bufferbloat.
Adaptive RED
✓ HAS IT
Adapts via max_p
mapping.
max_p → target
conversion.
Slow — 70s to
stabilise.
Only 1 of 4
params tuned.
PIE
✓ HAS IT
target=15ms
fixed in our
test config.
PIE adjusts
drop prob p,
not target
directly.
Statically set.
CAKE
✓ HAS IT
CAKE has internal
bandwidth shaping.
Target concept
exists internally.
4 params tuned
but preset —
not runtime
adaptive.
ACAPE (ours)
✓ HAS IT
5ms → 1.03ms
via AIMD β=0.9
15 adjustments.
HEAVY: ×0.9
LIGHT: +0.5ms
NORMAL: +0.2ms
[PREDICTIVE]
acts before peak.
Why this matters: Lower target means CoDel signals TCP earlier, keeping queue depth small. ACAPE is the only system that drives target from 5ms to 1ms dynamically under heavy load.
▶ Show the AIMD staircase graph here. 5ms → 1.03ms is your strongest visual proof. Static stays flat. Only ACAPE descends.

## Slide 3
Feature 2 of 12
Feature 2 of 12
Tunes fq_codel interval parameter
The interval is the CoDel observation window. CoDel only drops if sojourn exceeds target continuously for at least interval milliseconds. CoDel requires interval ≥ 10×target. If target changes, interval MUST also change or CoDel behaviour becomes inconsistent.
Static fq_codel
✗ MISSING
Fixed at 100ms.
Never changes.
Consistent with
target=5ms:
100 = 10×5
But if target
changed without
interval, CoDel
would misbehave.
Adaptive RED
✗ MISSING
Interval stays
at 100ms.
Only target
changes via
max_p mapping.
This breaks the
10×target rule
when target < 10ms.
PIE
✗ MISSING
PIE does not
use interval.
Different AQM
algorithm.
PIE uses
tupdate=30ms
for its PI
controller cycle.
CAKE
✓ HAS IT
CAKE manages
its own internal
timing parameters.
Not directly
exposed as
fq_codel interval.
Internal only.
ACAPE (ours)
✓ HAS IT
interval =
max(10×target,
50ms)
Enforced after
every AIMD step.
5ms→1ms:
interval goes
100ms→10ms.
CoDel stays
theoretically valid.
Why this matters: Without tuning interval alongside target, CoDel's behaviour becomes undefined. ACAPE is the only system that maintains the CoDel constraint interval≥10×target at all times.
▶ This is a subtle but important point. ARED only tunes target — it never touches interval. This means ARED violates the CoDel spec when target drops below 10ms.

## Slide 4
Feature 3 of 12
Feature 3 of 12
Tunes fq_codel limit parameter (queue depth ceiling)
The limit parameter is the hard ceiling on queue depth in packets. Packets beyond limit are tail-dropped immediately, before CoDel even evaluates them. Under heavy congestion, ACAPE reduces limit alongside target — a two-level defence against bufferbloat.
Static fq_codel
✗ MISSING
Fixed at 1024p.
Never changes.
Under 20-flow
load, queue
fills to 400+p.
Limit never
defends.
Only CoDel's
sojourn check
signals.
Adaptive RED
✗ MISSING
Limit stays
at 1024p.
Adaptive RED
was designed
for RED not
fq_codel.
Only max_p
(→target) is
adapted.
PIE
✗ MISSING
PIE uses
limit=1000p
fixed.
No runtime
adjustment.
PIE's drop prob
p handles
congestion
without touching
queue ceiling.
CAKE
✓ HAS IT
CAKE manages
queue depth
internally via
bandwidth shaping.
Not exposed as
fq_codel limit.
Effective but
not user-visible
at runtime.
ACAPE (ours)
✓ HAS IT
HEAVY regime:
limit × 0.9
1024 → 921
→ 829 → ...
Two-level defence:
1. CoDel drops
by sojourn
2. Limit drops
by ceiling
Both tighten
under congestion.
Why this matters: Reducing limit under heavy congestion provides a second defence against queue overflow. Even if CoDel is slow to signal, the ceiling shrinks. ACAPE uses both mechanisms simultaneously.
▶ Show the fq_codel Parameters panel from Grafana — you can see limit decreasing step by step alongside target. Two staircases descending together.

## Slide 5
Feature 4 of 12
Feature 4 of 12
Tunes fq_codel quantum parameter (DRR scheduling)
quantum defines how many bytes each flow may transmit per Deficit Round Robin scheduling turn. Default 1514 bytes = one Ethernet frame per turn. Smaller quantum = shorter turns = mice flows (DNS, HTTP/2) get served faster. Larger quantum = better for elephant flows (FTP, video).
Static fq_codel
✗ MISSING
quantum=1514B
forever.
One ETH frame
per DRR turn.
Mice flows wait
behind elephants
for full turns.
No flow-type
awareness.
Adaptive RED
✗ MISSING
quantum=1514B
fixed.
Adaptive RED
never touches
the DRR
scheduler.
Fairness is
DRR-default
not adaptive.
PIE
✗ MISSING
PIE has no
DRR scheduler.
Single FIFO
queue.
quantum concept
does not apply
to PIE.
All flows
share one queue.
CAKE
✓ HAS IT
CAKE has
per-flow DRR
with triple
isolation.
quantum is
managed internally.
Not user-tuned
at runtime —
preset at start.
ACAPE (ours)
✓ HAS IT
eBPF-driven:
elephant_ratio
< 0.2 → MICE
quantum=300B
0.2–0.6 → MIXED
quantum=1514B
> 0.6 → ELEPHANT
quantum=3000B
Changes live
as flows change.
Why this matters: This is ACAPE's unique C3 contribution. No other system adapts the DRR quantum from live per-flow eBPF data. At quantum=300B, a DNS query finishes in 1 DRR turn instead of waiting behind a 1500B elephant packet.
▶ This is where you say: CAKE has good per-flow scheduling but it's static. ACAPE changes quantum in real-time based on what traffic is actually flowing right now.

## Slide 6
Feature 5 of 12
Feature 5 of 12
Gradient-based congestion signals — C1
All other AQM systems ask: HOW congested is it NOW? ACAPE additionally asks: WHERE IS IT GOING? By computing the slope (gradient) of drop_rate, backlog, and RTT over the last 10 measurements, ACAPE detects whether congestion is worsening, stable, or recovering.
Static fq_codel
✗ MISSING
No gradient.
Compares current
queue vs threshold.
Binary decision:
above or below
5ms target.
No direction
detection.
Adaptive RED
✗ MISSING
No gradient.
Compares avg_q
vs target range.
Same philosophy
as Static:
react to current
condition only.
No trend.
PIE
✗ MISSING
PI controller
uses current
and previous
delay only.
Δdelay gives
a derivative
but NOT a
sustained trend
over 10 samples.
CAKE
✗ MISSING
No gradient
signals exposed.
CAKE reacts to
current queue
state internally.
No multi-sample
trend analysis.
No direction
detection.
ACAPE (ours)
✓ HAS IT
G(t) = 0.6·∇dr/30
+ 0.4·∇bl/300
∇ = slope over
W=10 samples
(5 seconds)
G>0.5 → WORSENING
G<-0.5 → RECOVERING
else → STABLE
3 signals fused:
drop_rate
backlog
RTT proxy
Why this matters: Gradient detection allows ACAPE to act on the DIRECTION of congestion, not just its current level. This is why ACAPE stabilises 12× faster than ARED — it detects worsening before the queue peaks.
▶ Show the Gradient Signals panel from Grafana. Point to the flat near-zero region (stable) and the spike when traffic ends. The system detected RECOVERING immediately.

## Slide 7
Feature 6 of 12
Feature 6 of 12
Predictive congestion control — C2
Reactive systems wait for congestion to arrive, then respond. ACAPE's [PREDICTIVE] mode detects a WORSENING gradient and acts on the PREDICTED next regime — applying a lighter correction before conditions deteriorate. This prevents overshoot.
Static fq_codel
✗ MISSING
Purely reactive.
Acts on current
condition only.
Waits for queue
to build before
responding.
No anticipation
of future state.
Adaptive RED
✗ MISSING
Purely reactive.
Same as Static
philosophy.
Acts every 500ms
but only on
current avg_q
vs target.
No prediction.
PIE
✗ MISSING
PI controller
has derivative
term (Δdelay).
This gives
some rate-of-
change awareness.
But not sustained
trend prediction
over 5+ seconds.
CAKE
✗ MISSING
No predictive
control.
CAKE reacts to
current traffic.
Advanced shaping
but still reactive
in nature.
No future-state
anticipation.
ACAPE (ours)
✓ HAS IT
if G(t) > 0.5:
WORSENING
→ use NEXT regime
→ [PREDICTIVE]
Example:
Current = MODERATE
Predicted = HEAVY
→ Apply HEAVY rule
BEFORE reaching
actual HEAVY
4 of 15 adjust-
ments were
[PREDICTIVE]
Why this matters: [PREDICTIVE] mode is the key reason ACAPE stabilises in <5s while ARED takes 70s. ARED waits for HEAVY to arrive. ACAPE acts while still in MODERATE, preventing the queue from peaking.
▶ This is your strongest novel contribution slide. Say: no prior AQM system in the literature predicts the next regime and acts on it. Show the [PREDICTIVE] log entries.

## Slide 8
Feature 7 of 12
Feature 7 of 12
eBPF in-kernel per-flow telemetry — C3
Extended Berkeley Packet Filter allows safe kernel programs that run at nanosecond speed without modifying kernel source. ACAPE attaches a TC egress hook to the router interface, measuring every packet and storing per-flow state in BPF maps accessible from userspace.
Static fq_codel
✗ MISSING
No eBPF.
Reads tc stats
only — aggregate
counters, no
per-flow data.
Blind to flow
composition:
can't detect
elephant/mice.
Adaptive RED
✗ MISSING
No eBPF.
Same limitation
as Static.
Aggregate tc
stats only.
max_p adapts
without knowing
which flows
caused congestion.
PIE
✗ MISSING
No eBPF.
PIE measures
queue departure
rate only.
Single aggregate
value — no
per-flow state
at all.
CAKE
✗ MISSING
No eBPF.
CAKE uses
hash-based
flow isolation
built into the
kernel qdisc.
No programmable
in-kernel hook
for telemetry.
ACAPE (ours)
✓ HAS IT
TC egress hook
on veth_rs.
BPF maps:
flow_map
(LRU_HASH 65536)
per-flow:
· byte count
· pkt count
· RTT EWMA
global_map
(PERCPU_ARRAY)
size_hist
(ARRAY 16 slots)
prog_id=49152
jited confirmed
Why this matters: eBPF gives ACAPE kernel-speed per-flow visibility with zero kernel modification. This is what makes C3 (workload profiles) possible — without eBPF, elephant/mice classification requires expensive userspace packet capture.
▶ Point to the Grafana eBPF Flow Classification panel. Show prog_id and jited flag. Explain: jited means JIT-compiled to native x86 — runs as fast as kernel code.

## Slide 9
Feature 8 of 12
Feature 8 of 12
Three-timescale control architecture — C4
Borkar 1997 proves that systems with multiple timescales converge if faster timescales are quasi-static from the slower one's perspective. ACAPE implements: T1 eBPF per-packet (~ns), T2 gradient estimation (500ms), T3 AIMD policy (~5s). Each level feeds the next.
Static fq_codel
✗ MISSING
Single timescale:
CoDel acts
per-packet
internally.
No external
control loop.
No separation
of measurement,
estimation, and
policy.
Adaptive RED
✗ MISSING
Single control
loop: 500ms.
Measures avg_q,
applies AIMD.
No separation
between sensing
and acting.
No kernel-level
instrumentation.
PIE
✗ MISSING
Single loop:
30ms (tupdate).
Fastest of all
five systems.
But single
timescale — PI
controller does
both sense and
act in one step.
CAKE
✗ MISSING
No explicit
timescale
separation.
CAKE's internal
algorithm runs
at qdisc level.
No userspace
control loop
or multi-layer
architecture.
ACAPE (ours)
✓ HAS IT
T1: eBPF (~ns)
· per-packet
· flow_map update
· RTT EWMA
T2: Python (500ms)
· read BPF maps
· gradient compute
· regime classify
T3: AIMD (~5s)
· update params
· tc qdisc change
· log adjustment
Borkar 1997
convergence proof
Why this matters: Three-timescale separation is theoretically grounded. T1 runs at kernel speed (no overhead). T2 aggregates over 5 seconds of history. T3 applies stable, non-oscillating updates. This prevents the instability seen in single-loop controllers under rapid traffic changes.
▶ This is the architecture slide. Draw T1→T2→T3 with arrows in the air. Say: 'each level is designed to be quasi-static from the level above it — this is Borkar 1997.'

## Slide 10
Feature 9 of 12
Feature 9 of 12
Elephant and mice flow classification
In networks, elephant flows are large long-lived transfers (FTP, video) and mice flows are small short-lived requests (DNS, HTTP/2, API calls). Under default DRR with quantum=1514B, both get equal turns — but mice flows finish in 1 turn while elephants need hundreds, causing mice to wait.
Static fq_codel
✗ MISSING
No flow
classification.
DRR treats all
flows equally:
quantum=1514B
per turn.
A 64-byte DNS
waits behind a
1500-byte video
packet equally.
Adaptive RED
✗ MISSING
No flow
classification.
Aggregate stats
only from tc.
No awareness of
how many small
vs large flows
are active.
PIE
✗ MISSING
No per-flow
scheduling.
PIE uses a
single queue.
All packets
mixed together
regardless of
flow size or
type.
CAKE
✓ HAS IT
CAKE classifies:
· tin-based
DiffServ
· per-flow
isolation
· host fairness
But classification
is preset at
startup — not
runtime adaptive
from live data.
ACAPE (ours)
✓ HAS IT
eBPF flow_map:
flows>1MB in
2s → elephant
r_e = elephant/
total flows
r_e < 0.2 → MICE
quantum=300B
r_e 0.2-0.6 → MIX
quantum=1514B
r_e > 0.6 → ELEPH
quantum=3000B
Live. Every 500ms.
Why this matters: ACAPE is the only system that dynamically classifies elephant and mice flows using live eBPF data and adapts the DRR quantum accordingly. At quantum=300B, a mice flow finishes its DRR turn in one small packet — 5× faster access than with default quantum.
▶ CAKE classifies but statically. ACAPE classifies live, every 500ms, and changes quantum accordingly. If your traffic shifts from FTP to DNS queries, ACAPE adapts automatically.

## Slide 11
Feature 10 of 12
Feature 10 of 12
Zero kernel source modification
Many AQM research systems require patching the Linux kernel source, recompiling, and rebooting. This makes deployment impossible on production systems. ACAPE uses only standard Linux interfaces: tc qdisc change, eBPF TC hook via clsact, and bpftool — all available on Ubuntu 24.04 LTS.
Static fq_codel
✓ HAS IT
No kernel mod
needed.
tc qdisc add
fq_codel is a
standard Linux
command since
kernel 3.5.
Works on any
Linux system
out of the box.
Adaptive RED
✗ MISSING
Original ARED
was designed
for simulation.
Our implementation
maps max_p to
fq_codel target
via userspace.
No kernel patch
but not the
original design.
PIE
✓ HAS IT
PIE is in
mainline Linux
kernel.
modprobe sch_pie
enables it.
No source
modification
needed.
Standard tc
interface.
CAKE
✓ HAS IT
CAKE is in
mainline Linux
kernel.
modprobe sch_cake
enables it.
No source
modification
needed.
Standard tc
interface.
ACAPE (ours)
✓ HAS IT
Zero kernel
modification.
Only uses:
· tc qdisc add
· tc filter add
bpf direct-
action
· tc qdisc change
· bpftool map dump
All standard
Linux tools.
No recompile.
No reboot.
Why this matters: Deployability matters. A system requiring kernel recompilation cannot be deployed on cloud VMs, ISP routers, or production servers. ACAPE works on any Ubuntu 24.04 system with root access — no vendor coordination needed.
▶ This is a practical contribution. Our entire system can be started with: sudo bash master_run.sh — on any Linux machine. No kernel patches, no reboots.

## Slide 12
Feature 11 of 12
Feature 11 of 12
Live Prometheus + Grafana monitoring
Production-grade observability: 28 metrics exported every 2 seconds to Prometheus, visualised in a Grafana dashboard with 21 panels. Shows eBPF status, all four fq_codel parameters, gradients, regime, predicted regime, Jain fairness, sojourn time, topology diagram, and algorithm summary.
Static fq_codel
✗ MISSING
No live monitoring.
Only: tc -s
qdisc show
(manual command).
No time-series.
No dashboard.
No alerts.
Results only
from iperf3
log files.
Adaptive RED
✗ MISSING
No live
monitoring.
Same as Static:
tc stats only
via command line.
No Prometheus
exporter.
No Grafana
dashboard.
PIE
✗ MISSING
No live
monitoring.
PIE exposes
no additional
metrics beyond
standard tc
stats.
No dashboard.
CAKE
✗ MISSING
No live
monitoring.
CAKE's stats
are tc-visible
but no Prometheus
exporter exists
for CAKE-specific
metrics.
No dashboard.
ACAPE (ours)
✓ HAS IT
28 metrics
exported:
· eBPF status
· prog_id
· target/interval
limit/quantum
· backlog pkts/bytes
· drop rate
· throughput
· gradients C1
· regime/predicted
· Jain fairness
· sojourn/latency
· flow counts
· workload profile
Grafana: 21 panels
Prometheus: port 9101
Refresh: every 5s
Why this matters: Live monitoring transforms ACAPE from a research prototype into a production-observable system. Any operator can see exactly what the controller is doing and why, in real time. This is what companies like Cloudflare and Meta use for eBPF in production.
▶ Show your Grafana screenshot. Say: everything you see here updates every 5 seconds during the live experiment. This is not post-processed — it is real-time.

## Slide 13
Feature 12 of 12
Feature 12 of 12
Router topology — ISP edge deployment model
A two-node topology (client ↔ server) tests endpoint AQM. A three-node router topology (client → router → server) tests AQM at a forwarding device — the realistic deployment model for ISP edge routers, home gateways, and datacenter switches.
Static fq_codel
✓ HAS IT
Tested in our
experiment on
router topology.
ns2 → ns_router
→ ns1
Static params
on router egress.
Represents:
current state
of all Linux
routers.
Adaptive RED
✓ HAS IT
Tested in our
experiment on
router topology.
Controller runs
in userspace on
the router host.
Matches Floyd
2001 topology:
single bottleneck
multiple sources.
PIE
✓ HAS IT
Tested in our
experiment on
router topology.
PIE qdisc
applied to
router egress
interface.
RFC 8033 designed
for router AQM.
CAKE
✓ HAS IT
Tested in our
experiment on
router topology.
CAKE applied
to router egress
with bandwidth
shaping.
CAKE was designed
for home router
deployment.
ACAPE (ours)
✓ HAS IT
ns2(192.168.1.2)
↓ veth_cr
ns_router
192.168.1.1
192.168.2.1
TBF 5Mbit
fq_codel
eBPF hook
↓ veth_rs
ns1(192.168.2.2)
AQM on router
egress — exactly
how ISP routers
deploy AQM.
Why this matters: Router topology is the correct experimental model. An ISP router, not an endpoint, performs AQM. All five systems are tested on the same three-node topology ensuring fair comparison.
▶ All five systems ran on identical topology: ns2 → ns_router → ns1. Same TBF 5Mbit bottleneck. Same 20 TCP CUBIC flows. Fair comparison — only the qdisc and controller differ.

## Slide 14
Feature Summary — Final Score
Static fq_codel
3/12 features
Has:
✓ No kernel mod
✓ Router topology
✓ CoDel internal
Missing:
✗ Tunes target
✗ Interval
✗ Limit
✗ Quantum
✗ +6 more
Adaptive RED
3/12 features
Has:
✓ Tunes target (1 param)
✓ Router topology
✓ AIMD philosophy
Missing:
✗ Interval
✗ Limit
✗ Quantum
✗ Gradient
✗ +6 more
PIE
4/12 features
Has:
✓ Tunes drop prob
✓ No kernel mod
✓ Router topology
✓ Delay-based ctrl
Missing:
✗ Tunes target
✗ Interval
✗ Limit
✗ Quantum
✗ +6 more
CAKE
6/12 features
Has:
✓ 4 params (internal)
✓ No kernel mod
✓ Router topology
✓ Flow isolation
✓ DiffServ
✓ Fairness
Missing:
✗ Gradient
✗ Predictive
✗ eBPF
✗ 3-timescale
✗ +2 more
ACAPE
12/12 features
Has:
✓ All 12 features
ACAPE scores 12/12 — the only system combining gradient prediction, eBPF telemetry, predictive control, and full parameter tuning on stock Linux.
▶ End here. Say: across 12 features, ACAPE is the only complete system. Every other system has gaps. That is the contribution.