## Slide 1
All Features — 5 Systems on One Slide
Static
fq_codel
Adaptive
RED
PIE
CAKE
ACAPE
(ours)
Tunes target param
✗
✗
✗
✗
✓
Tunes interval param
✗
✗
✗
✓
✓
Tunes limit param
✗
✗
✗
✓
✓
Tunes quantum param
✗
✗
✗
✓
✓
Gradient signals (C1)
✗
✗
✗
✗
✓
Predictive control (C2)
✗
✗
✗
✗
✓
eBPF per-flow telemetry (C3)
✗
✗
✗
✗
✓
3-timescale architecture (C4)
✗
✗
✗
✗
✓
Elephant/mice profiling
✗
✗
✗
✗
✓
No kernel modification
✓
✗
✓
✓
✓
Live Prometheus monitoring
✗
✗
✗
✗
✓
Router topology tested
✗
✓
✓
✓
✓
Score (out of 12)
1/12
3/12
3/12
5/12
12/12
▶ SPEAK: ACAPE scores 12/12. Every other system has gaps. This single slide is the clearest argument for why ACAPE is novel.

## Slide 2
Comparison 1: ACAPE vs Static fq_codel
Static fq_codel — No Algorithm
Parameters fixed at boot — never change.
target=5ms interval=100ms limit=1024 quantum=1514
No runtime controller. No measurement loop.
CoDel drops internally when sojourn>5ms.
Queue builds to 400+ packets — bufferbloat.
ACAPE — What Changes
target
5ms → 1.03ms (15 AIMD steps, β=0.9)
interval
10×target, enforced each step
limit
1024 → 921 → ... (×0.9 each HEAVY)
quantum
1514 → 300B when MICE detected
[INSERT PLOT: comparison_key_result.png — BACKLOG panel]
[INSERT PLOT: comparison_key_result.png — TARGET panel]
ACAPE wins vs Static
28% lower backlog · 12× faster stabilise · throughput highest
ACAPE loses vs Static
Higher drop rate · Higher sojourn · More complex system
▶ SPEAK: Static is the status quo on every Linux system. ACAPE beats it on every adaptive metric. The only 'advantage' static has is simplicity.

## Slide 3
Comparison 2: ACAPE vs Adaptive RED
Adaptive RED — Base Paper Algorithm
Floyd, Gummadi, Shenker 2001 — ICSI Technical Report
Tunes max_p every 500ms using AIMD (β=0.9)
max_p maps to fq_codel target parameter only
3 params FIXED: interval, limit, quantum
No gradient direction — only current vs threshold
No per-flow awareness — no eBPF
Stabilises in ~70 seconds
Avg backlog: 412 packets
ACAPE — What We Add on Top
Inherits
AIMD structure β=0.9 (same as ARED)
Inherits
500ms adaptation philosophy
ADDS C1
Gradient signals — direction, not just level
ADDS C2
Predictive: acts before congestion peaks
ADDS C3
eBPF: elephant/mice quantum selection
ADDS C4
Three-timescale: eBPF+gradient+AIMD
ADDS
Tunes ALL 4 params, not just target
[INSERT PLOT: comparison_all_params.png — DROP RATE panel]
[INSERT PLOT: comparison_all_params.png — TARGET panel]
ACAPE wins vs ARED
24% lower backlog · 12× faster stabilise · 4 params tuned vs 1
ACAPE loses vs ARED
Higher sojourn time · Higher complexity · Harder to deploy
▶ SPEAK: ACAPE IS Adaptive RED — extended. Same AIMD heart, but with gradient direction, prediction, and eBPF. We cite Floyd 2001 as our base paper and show we beat it.

## Slide 4
Comparison 3: ACAPE vs PIE
PIE — Proportional Integral Enhanced
RFC 8033 — Control-theoretic approach
PI controller: p += α(delay-target) + β(Δdelay)
α=0.125 β=1.25 — classical control gains
Adjusts drop probability p every 30ms (very fast)
No per-flow scheduling — single queue, no DRR
target=15ms fixed limit=1000p fixed
Achieves very low backlog ~5-8 packets
Achieves very low sojourn ~6ms
ACAPE vs PIE — Key Differences
PIE has
No per-flow fairness (no DRR)
PIE has
No gradient direction detection
PIE has
Static target and limit — never adapts
ACAPE has
DRR per-flow isolation via fq_codel
ACAPE has
Gradient: knows if WORSENING/RECOVERING
ACAPE has
quantum adapts — 300B for mice flows
ACAPE has
Higher throughput despite higher sojourn
[INSERT PLOT: comparison_summary_bars.png — BACKLOG bars]
[INSERT PLOT: comparison_summary_bars.png — SOJOURN bars]
ACAPE wins vs PIE
Higher throughput · Per-flow fairness · Gradient direction · 4 params tuned
ACAPE loses vs PIE
PIE: lower backlog (~6p) · much lower sojourn (~6ms) · faster response (30ms vs 500ms)
▶ SPEAK: PIE achieves lower latency. That is a real advantage. Our response: ACAPE optimises throughput-first. PIE's 30ms update risks instability under burst loads.

## Slide 5
Comparison 4: ACAPE vs CAKE
CAKE — Controlled/Advanced Kitchen Engine
bufferbloat.net — modern fq_codel successor
Combines: AQM + shaping + fairness in one qdisc
Bandwidth shaping: cake bandwidth 5mbit
DiffServ classification: diffserv4 flag
Triple isolation: flow, host, and tin fairness
wash: removes DSCP marks (prevents gaming)
flowblind: hash-based per-flow isolation
Achieves lowest backlog ~5p, sojourn ~17ms
ACAPE vs CAKE — Key Differences
CAKE
Requires bandwidth param at setup
CAKE
Static — no runtime parameter adaptation
CAKE
No gradient signal — reactive only
CAKE
No eBPF telemetry — no per-flow ML
ACAPE
Runtime adaptation — no config needed
ACAPE
Gradient-based — detects direction
ACAPE
eBPF: live per-flow classification
[INSERT PLOT: comparison_all_params.png — BACKLOG time panel]
[INSERT PLOT: comparison_feature_matrix.png]
ACAPE wins vs CAKE
Runtime adaptive · No prior bandwidth config · Gradient direction · eBPF per-flow
ACAPE loses vs CAKE
CAKE: lower backlog · lower sojourn · better inbuilt DiffServ · mature production tool
▶ SPEAK: CAKE is the strongest baseline. Acknowledge it. ACAPE's advantage: CAKE needs bandwidth pre-configured. ACAPE adapts automatically — no human config needed.

## Slide 6
Honest Evaluation: Where ACAPE Falls Short
Sojourn Time — Higher than PIE and CAKE
WHAT: ACAPE sojourn ~63ms vs PIE ~6ms vs CAKE ~17ms
WHY: ACAPE allows controlled queue depth to maintain throughput. Aggressive dropping (PIE/CAKE) reduces sojourn but risks underutilising the link.
DEFENCE: This is a deliberate tradeoff — throughput-first design. For latency-critical apps (VoIP, gaming), PIE/CAKE would be better choices.
RTT Gradient Signal — Currently Flat
WHAT: ∇RTT_proxy = 0 throughout. eBPF flow_map reads return empty across namespace boundary.
WHY: bpftool cross-namespace map export issue. The eBPF program IS running (prog_id confirmed, jited, quantum=300B fires) but userspace can't read per-flow RTT data.
DEFENCE: Fix identified: pin bpf_link with explicit namespace fd. C1 still functions with ∇drop_rate and ∇backlog — RTT is future work.
Jain Fairness — Slightly Reduced
WHAT: ACAPE Jain index slightly below 0.9997 baseline under MICE profile
WHY: When quantum=300B (MICE), DRR scheduling weights shift. Short flows complete faster, long flows get fewer turns — strict per-flow equality breaks.
DEFENCE: This is intentional: ACAPE prioritises latency for short flows (C3 contribution). Absolute fairness is not the design goal.
Complexity — Harder to Deploy
WHAT: Requires eBPF compilation, clang, bpftool, Python controller, Prometheus, Grafana
WHY: Each system component adds a failure point. Static fq_codel works with one tc command. ACAPE requires ~8 components running simultaneously.
DEFENCE: This is a research prototype. Production hardening (packaging as a single daemon) is future work. The academic contribution is the architecture.
▶ SPEAK: Present these proactively — don't wait to be asked. Say 'We are aware of these limitations.' It shows maturity and pre-empts reviewer questions.

## Slide 7
All Comparison Plots — From Live Experiment
[INSERT PLOT: comparison_key_result.png]
Backlog + Target over time
[INSERT PLOT: comparison_summary_bars.png]
Avg metrics — all 6 bars
[INSERT PLOT: comparison_latency_cdf.png]
Latency CDF curves
[INSERT PLOT: comparison_all_params.png]
All 9 parameters — time series
[INSERT PLOT: comparison_feature_matrix.png]
Feature matrix ✓/✗
[INSERT PLOT: comparison_droprate.png]
Drop rate comparison
▶ SPEAK: After master_run.sh finishes: python3 scripts/plot_all_systems.py --logdir logs/ --plotdir plots/ — then drag each PNG into these boxes.